## Slide 1: Air filter inspection
Pgss automotive 11/12

## Slide 2: Equipment needed
Safety goggles
Trouble light
shop towel or rag

## Slide 3: Locate the air box
Raise the hood
Locate the air box
Usually a big black square or rectangle
Remove or disconnect hold down clips or screws

## Slide 4: Disconnect hold down clips

## Slide 5: Remove air filter
Carefully note the position of the filter
Right side up / upside down
Take a photo if necessary this will help with a reinstall

## Slide 6: The air filter revealed

## Slide 7: Carefully remove the filter

## Slide 8: Checking the air filter with a trouble light

## Slide 9: Does the filter pass or fail?
Shine a light behind the filter
Can you see lots of light through it
Pass
If little or no light passes through
Fail
What are your results?

## Slide 10: Tap out the filter on the floor or bench
Recheck the filter with the trouble light
Press play

## Slide 11: Replace air filter as necessary
vehicle information is needed for the correct air filter replacement
year
Make
Model
Engine size
Contact a parts supplier with the information to obtain a new filter.

## Slide 12: New filter

## Slide 13: Reinstall air filter in proper air box location

## Slide 14: Reinstall air box lid
Check the fit of the lid
Secure the latches
You’re good to go

## Slide 15
Submit results to Mr. G