## Slide 1: Oil change
Pgss auto 11/12

## Slide 2: Safety safety safety
No watches
No rings
No dangly things
No hoodie strings
Safety goggles
safety goggles
safety goggles

## Slide 3: Equipment needed
3/8 drive ratchet
3/8 drive socket. The right size to fit the drain plug on oil pan
Oil filter wrench or socket to fit the vehicles oil filter
Trouble light
Drain bucket
funnel

## Slide 4
Equipment Needed

## Slide 5: Vehicle information needed
YEAR
MAKE
MODEL
ENGINE SIZE
OF THE VECHILE YOU ARE WORKING ON

## Slide 6: Parts needed
ENGINE OIL
ENGINE OIL FILTER
CONTACT A PARTS SUPPLIER WITH THE VEHICLE INFORMATION YOU OBTAINED IN THE PREVIOUS SLIDE
THIS WILL ENSURE YOU GET THE CORRECT TYPE AND AMOUNT OF ENGINE OIL AND THE CORRECT ENGINE OIL FILTER FOR YOUR VEHICLE

## Slide 7: PARTS NEEDED

## Slide 8: Procedure ALL RIGHT LET’S GET STARTED

## Slide 9: Step 1 bring the car up to operating temperature THIS WILL ENSURE THAT ALL Contaminants WILL BE STIRRED UP AND TRAPPED IN THE OIL ONCE VEHICLE IS UP TO TEMP SHUT OFF AT THIS POINT ENGINE OIL AND ALL PARTS WILL BE EXTREMLY HOT ! USE SAFETY GOGGLES AND CAUTION AT ALL TIMES

## Slide 10: Step 2 LOCATE OIL PAN AND DRAIN PLUG ON THE UNDERSIDE OF THE ENGINE

## Slide 11: STEP 3 PLACE drain bucket under oil pan loosen drain plug ratchet and socket should be turned counter clockwise
PLAY ME!

## Slide 12: Step 4 remove drain plug CAUTION REMEMBER THE OIL IS EXTREMLY HOT
PLAY ME !

## Slide 13: Step 5 drain oil
Play Me!

## Slide 14: Step 6 clean and reinstall drain plug

## Slide 15: Step 7 remove oil filter use an oil filter socket or wrench
PLAY ME

## Slide 16: Step 8 install new oil filter be sure to lube the rubber seal on the new filter install the filter hand tight only

## Slide 17: Step 9 add the correct TYPE AND amount of new oil
PLAY ME !

## Slide 18: Step 10 start vehicle and check for oil leaks look around the drain plug and filter

## Slide 19: Step 11 shut off vehicle and wait a minute or two check oil level with engine off adjust as necessary

## Slide 20: Step 12 clean up your area dispose of old oil and filter at a proper waste facility recycle oil containers if possible record and submit your results to mr g WELL DONE !